Jersey Tactical Corp.

201 Strykers Road

Suite 19 PO #331

Lopatcong, NJ 08865-5400

Phone: 908-995-2700

Website: www.jerseytactical.com

JTC-AR 500 Reactive Steel Target System Instructions

Thank you for your purchase of the JTC Target System. The target system is designed for long term use and abuse like all JTC products. Please follow the following maintenance schedule and safety guidelines. You can also visit the JTC Home page and view videos of this product being assembled and used.

WARNING: Do not use this target system without Ansi rated Eye protection, Gloves, and wearing long sleeve shirts and full length pants. Do not shoot the following Ammo on the target system, Hollow point pistol Ammo, any and all bonded or trophy bonded Ammo, Green Tip (M855). This target system is designed for all duty style pistols excluding the FN 5.7 or pistol calibers above a 357 Magnum. The system is designed to be used with the M-4 Platform, use of a higher caliber rifle platform such as 300 Win/Mag etc will result in damage to your targets

Stand Off Distances: In order to minimize splash back and possible injury to the end user the following minimum standoffs are required. Pistol 15 yards and Rifle 50 yards.

WARNING: These distances are from the target while facing the target system. NEVER BE LATERIAL TO THE TARGETS WHILE THEY ARE IN USE PERIOD!!!!

Assembly: The steel stands are designed to be placed into one another for assembly and disassembly in seconds. The stands should be set up with the long portion of the H base facing towards the shooter. Next the long vertical support slides into the center opening of the H Base. Note the vertical support should have the heavy V facing towards the shooter. Next place the rear angled steel leg located on the rear of the target into the opening at the top of the vertical support.

WARNING: The stand and the target are held together with gravity. When moving disassemble in the reverse order and do not attempt to move the assembled stand for the pieces may become dislodged. Next do not place targets on extreme angles due increase risk of splash back or the target simply falling over.

Storage: The stands can remain out 365 a year please note that they are steel and they will eventually rust due to the long term exposure to the weather. JTC Suggest using a pair of medical gloves when moving the targets due lead covering all portions of the targets system once they are in use. The gloves should not be used again after you have finished setting up or taking down the target system.

WARNING: Targets should never be left out in the weather and should not be dropped onto hard surfaces. When storing the targets place them into storage.

Maintenance: The targets can be painted with any spray paint you wish. It is suggested that you touch up the bases as well for long term overall appearance and maintenance. The edge of the AR 500 are hard steel but due to the exposure of the interior steel on the edge they can produce grooves from rounds.

WARNING: Inspect your targets before and after each use in order ensure the safety of all. If a groove or raised piece appears on the target place the target out of service until you can use an angle grinder to remove said burr or grove. Once this is done coat exposed area with spray paint.

Location of Targets: The JTC Target System is designed to produce audio and visible feedback clearly out to 200 yards. The system is also designed to throw the majority of the round downward and even backwards. Please keep this in mind when selecting you back stop for this system. Also please be aware that portions of the rounds can fragment upwards and forward from the target and could cause damage to an indoor range and or lighting.

WARNING: The JTC Reactive Steel Target System will produce splash back as will all steel targets. Users use the JTC Reactive Steel Target System at their own risk and JTC is not responsible for any and all injuries or deaths associated with such uses.