Jersey Boot Vehicle Mount Installation Instructions

The Vehicle Mount can be attached with a wide variety fasteners or by welding it to a steel surface. The Vehicle Mount should be mounted on a secure surface that will not be compromised by severe impact during a crash. The Mount should not be attached to any trunk lid or door surface in any vehicle. The Vehicle Mount shall be installed as low as possible to the floor board area if installed in a large open area that also will transport humans. Under this application the Vehicle Mount should be mounted with the steel supports of the mount facing forward in case of a severe head on crash. The Vehicle mount should always be installed so that the steel material of the mount supports the majority of the weight of the Jersey Boot while being hung and or attached to a bulkhead, floor and or other surface.

Warning:

- Do not attach in close proximity to fuel sources or electrical sources.

- All installations must be completed by a certified service mechanic for agency and or military.

- Any and all opinions about where to safely attach the Jersey Boot Vehicle Mount are to be recommended by the manufacturer of the vehicle you are attaching the Vehicle Mount to.

- Avoid drilling and using self taping screws in blind enclosed areas where you are unsure of what is beneath the surface you are drilling into.  It is strongly recommended that you do not attach the Vehicle Mount this way.

- Any and all Vehicle Mounts can be secured via welding, case hardened bolts, washers and nylon locking nuts, or commercial grade molly bolts.

- Jersey Tactical Corp is not responsible for any damage or caused to the vehicle during the installation of this product.

- Consult the manufacturer of your vehicle on any and all questions you have.

- Jersey Tactical Corp. insists that all installers consider how the mount will react during a severe collision and mass transfer of energy. For this reason Jersey Tactical Corp. advises the mounting system should be secured in an area absent of humans during transportation.

- Jersey Tactical Corp. is not responsible for any injury or damage caused by improper installation or use of the Vehicle Mount.